## Slide 1
INDUSTRIAL COMPUTER VISION
Dent & Scratch Defect Inspection — Back Glass
Traditional CV development + future Deep Learning / Hybrid roadmap
CURRENTLY UNDER TEST
Interpretable, tunable Traditional CV pipeline
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 2
Inspection Problem & Target
Detect small surface defects on reflective smartphone back glass while controlling glare, texture and temporal noise.
02
DEFECT TYPES
• Scratch: thin high-frequency structure / line
• Dent: localized surface deformation / intensity anomaly
• Both can be confused with glare, texture, dust or sensor noise
CORE CHALLENGES
• Reflective glass → illumination-sensitive response
• Micro-defects → very small spatial footprint
• Video inspection → false detections can flicker frame-to-frame
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 3
Current Inspection-Stations Architecture
The supplied application already provides a modular base for controlled image acquisition and pluggable detection.
03
CAMERA
Basler Camera 1/2 Exposure • Gain • FPS • Resolution
LIGHTING
RGB recipes Dual 4CH / Single 8CH
CAPTURE
Light ON → settle → capture → Light OFF → save
DETECTION
RAW Laplacian • Canny pluggable registry
UI / RESULT
Live view • parameters Detection result
Modularity allows new CV or DL detectors to be added without redesigning camera / lighting / capture control.
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 4
Three-Path Development Strategy
A staged approach: exhaust interpretable CV improvements, then introduce learned representations where required.
04
01
TRADITIONAL CV
Current testing Deterministic + tunable
02
DEEP LEARNING
Future fallback if handcrafted features are insufficient
03
CV + DEEP LEARNING
Hybrid CV-derived feature space → learned model
Decision point → compare detection stability, false-positive rate, minimum detectable defect size and production throughput.
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 5
Option 1 — Traditional CV: Phasewise Evolution
Each iteration addresses a specific failure mode observed in defect detection.
05
P1
Baseline
Gray → Laplacian → threshold → contours
Simple edge / micro-variation detector
P2
Noise reduction
Gaussian smoothing → Laplacian → mean + k·σ
Reduce high-frequency noise
P3
ROI awareness
CLAHE → Canny / Adaptive Threshold → contour ROI → erosion
Inspect relevant glass region; protect borders
P4
Spatial filtering
Candidate centroids → neighborhood radius → neighbor-count outlier logic
Reject repetitive glare / texture clusters
P5
Temporal stability
Local μ/σ via boxFilter → rolling mask buffer → persistence hits
Reduce frame-to-frame flicker
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 6
Traditional CV — Early Baseline: Laplacian + Dynamic Threshold
The first implementation converts local intensity curvature into a binary defect candidate map.
06
CORE OPERATION
• Convert BGR → grayscale
• Optional Gaussian smoothing to suppress sensor noise
• Laplacian: second spatial derivative / high-frequency response
• Threshold using mean + k × standard deviation
• Contours / bounding boxes group candidate pixels
Limitation: a single global threshold can move with illumination, texture and frame noise.
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 7
Traditional CV — ROI & Local Contrast Enhancement
Focus computation on the phone/glass region and make micro-contrast more visible before defect extraction.
07
1
CLAHE
Local histogram equalization Enhances micro-contrast without relying only on global brightness
2
ROI extraction
Gaussian blur → Canny / Adaptive Threshold → contours Area filtering selects major structural region
3
ROI erosion
5×5 morphology shrinks mask inward Separates interior defect analysis from border structure
Result → defect detector sees the relevant surface rather than the entire camera frame.
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 8
Traditional CV — Spatial Density Outlier Logic
A candidate is evaluated against nearby candidates: isolated anomalies are retained; dense repeating patterns are treated as likely texture / glare.
08
SPATIAL MODEL
Virtual neighborhood radius
IMPLEMENTATION LOGIC
• Extract contour centroids (x, y)
• Compute Euclidean distance to other candidates
• Count neighbors within search radius
• If neighbor count ≤ max_allowed → retain as isolated anomaly
• Apply separately to interior and edge candidates
Purpose: suppress repeating reflection / texture hits.
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 9
Traditional CV — Local Statistics + Temporal Persistence
The latest detector directly targets the two observed sources of flicker: global threshold drift and single-frame noise.
09
LOCAL Z-SCORE STYLE THRESHOLD
T(x,y) = μ_local(x,y) + k · σ_local(x,y)
• μ and σ computed with cv2.boxFilter on |Laplacian|
• Pixel must stand out from its own neighborhood
WHY IT HELPS
• Global threshold: sensitive to frame-wide drift
• Local threshold: adapts to nearby texture / illumination
• Rolling buffer: retains persistent hits
• Example: 3-frame buffer, require ≥2 hits
TEMPORAL FILTER
Rolling mask buffer → persistent candidate = stable defect; one-frame blip = rejected.
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 10
Option 1 — Current Target Pipeline
The working direction combines the strongest elements developed across the supplied implementations.
10
Controlled capture → CLAHE → ROI / border separation → Laplacian → local threshold → spatial outlier filter → temporal persistence → PASS / FAIL
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 11
Traditional CV — Key Parameters to Tune
Parameters map directly to physical defect size, optical noise and camera behavior.
11
CLAHE grid / clip
Local contrast scale
Too local → texture amplification; too broad → micro-defect contrast lost
Laplacian ksize
Spatial derivative scale
1/3/5/7 trades micro-detail vs robustness
k × σ
Detection sensitivity
Higher k → fewer candidates; lower k → higher sensitivity + more noise
ROI erosion
Border exclusion
Protects structural edges from being interpreted as defects
Neighborhood radius
Physical inspection area
Should map to calibrated pixel/mm scale
Max neighbors
Outlier criterion
Reject dense repetitive candidates
Window size
Local statistics context
Controls what 'local background' means
Persistence frames / hits
Temporal stability
Suppresses transient sensor / illumination noise
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 12
Option 2 — Deep Learning (Future Fallback)
Use learned visual representations when rule-based features cannot achieve required robustness.
12
INPUT
Controlled images
SEGMENTATION
Phone / glass ROI
DETECTOR
YOLO / instance detector
CLASSIFY
Dent / Scratch / OK
• Training data: defect / non-defect images with bounding boxes or masks
• Segmentation can isolate glass surface before detection
• Augmentation should model realistic lighting, glare and small-defect variation
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 13
Option 3 — Traditional CV + Deep Learning Hybrid
Use classical vision to expose physically meaningful attributes, then let a model learn the final representation / decision.
13
ENHANCED FEATURE SPACE
• Original RGB / grayscale appearance
• CLAHE-enhanced image
• Laplacian / gradient response
• Local mean, standard deviation / Z-score
• ROI, edge distance and morphology-derived masks
• Spatial density / persistence attributes
[raw image + engineered channels / attributes] → CNN / segmentation / detector → defect probability
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 14
Approach Comparison — What Each Path Adds
Use measurable inspection criteria to select the production direction.
14
Traditional CV
• Interpretable rules
• Fast to iterate
• Low data requirement
• Sensitive to imaging / thresholds
Deep Learning
• Learns complex appearance
• Handles variation with enough data
• Requires labeling + training
• Needs validation for small defects
CV + Deep Learning
• Retains engineered physical cues
• Richer input representation
• Potentially more robust
• Higher system complexity
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 15
Validation Plan — From Prototype to Production
Evaluate the inspection system against the physical defect requirement, not only visual examples.
15
A
Build defect set
Known dents + scratches Different positions / sizes
B
Optical repeatability
Multiple captures per part Lighting / exposure variation
C
CV tuning
Sensitivity vs false positives Pixel/mm calibration
D
DL benchmark
Train segmentation / detector Compare on held-out set
E
Production test
Cycle time • stability PASS/FAIL reliability
KPIs → Detection rate • False-positive rate • Minimum detectable defect • Processing time • Frame stability
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision

## Slide 16
Next Steps
Concrete work packages for the inspection development.
16
01
Optical setup
Fix camera pose, focus, exposure and controlled RGB lighting recipes.
02
Traditional CV
Tune CLAHE, ROI, Laplacian, local threshold, spatial + temporal filters.
03
Ground truth
Create labeled defect library with size / location / defect type metadata.
04
DL baseline
Train segmentation + detector on the same controlled capture protocol.
05
Hybrid experiment
Compare raw-image input vs CV-enriched multi-channel feature input.
06
Productionization
Integrate chosen detector into modular GUI and measure cycle-time / stability.
Phone Back-Glass • Dent & Scratch Inspection
Computer Vision